## Slide 1
Wire We Doing This?
Building IoT Systems from Scratch
F-Con 2025

## Slide 2
Meet Your Presenters
John Owen
Director, Security & Data Analytics
Fulcrum Technology Solutions
Ajay Patel
Senior Security Consultant
Fulcrum Technology Solutions

## Slide 3
What You Need: Software Setup
Before we dive into building, let's get our software tools ready. You'll need the Arduino IDE to write and upload code to your board, and access to our GitHub repository for all the project files.
Install Arduino IDE
Download and install the latest version of the Arduino IDE for your operating system. This software is essential for writing and uploading code to your Arduino board. Follow the on-screen instructions for a smooth installation.
https://www.arduino.cc/en/software/
Access the Code
All the code, diagrams, and additional resources for today's workshop are available on our dedicated GitHub repository. You can clone or download the files from here:
github.com/Fulcrum-Technology-Solutions/fcon_2025_iotoys

## Slide 4
Today's Journey
What We're Building:
Phase 0: Power test & connectivity (Setup)
Phase 1: Blink an LED (Crawl)
Phase 2: Button control with feedback (Walk)
Phase 3: Distance-sensing proximity alarm (CHAOS)
The Goal: Understand how sensors, processors, and outputs work together to create IoT systems

## Slide 5
What's In Your Kit?
Key Components We're Using Today:
Arduino Uno - Your programmable brain
Breadboard & Prototype Shield - Your workspace
Power Supply Module - Clean 5V power distribution
Red LED - Visual output
Active Buzzer - Audio alerts
Push Button - User input
HC-SR04 Ultrasonic Sensor - Distance measurement
4-Digit 7-Segment Display - Numerical readout
74HC595 Shift Register - Efficient display control
Supporting cast: 220Ω resistors, jumper wires
… and much more!

## Slide 6
Arduino 101
What is Arduino?
A microcontroller board that:
Reads inputs (buttons, sensors, signals)
Processes information (runs your code)
Controls outputs (lights, displays, buzzers)
Why Arduino?
Easy to learn
Massive community support
Powers everything from hobby projects to commercial products

## Slide 7
The IoT Building Block Concept
SENSOR
Gather information (distance, temperature, motion)
PROCESSOR
Make decisions (Arduino analyzes the data)
OUTPUT
Take action (displays, buzzers, lights)
Every IoT device follows this pattern. Today you'll build increasingly complex systems using this exact pattern.

## Slide 8
Setup Check: Arduino IDE
01
Install Arduino IDE
Download the latest version for your OS and follow the standard installation process.
02
Connect Uno R3
Plug your Arduino board into your computer with the USB A-to-B cable. Drivers should install automatically.
03
Configure Board & Port
In the IDE, go to Tools → Board → Arduino AVR Boards → Arduino Uno and then Tools → Port to select your Arduino's serial port.
If the upload fails, double-check your board and port selections. The Uno R3 is designed for easy setup!

## Slide 9
Setup Check
Before We Start:
Kit contents verified
Arduino IDE installed and open
Arduino connected via USB
GitHub repository link ready
ALL THE WIRES
GitHub Resources: https://tinyurl.com/5fan5erw All code, wiring diagrams, and troubleshooting guides
https://github.com/Fulcrum-Technology-Solutions/fcon_2025_iotoys

## Slide 10
Phase 0 - Power Test (Setup)
Goal:
Verify everything is connected and powered correctly
What You're Learning:
Breadboard power distribution
Arduino connectivity
Serial communication basics
Why This Matters:
A solid power foundation prevents 90% of problems!

## Slide 11
CRITICAL STEP: Set Power Jumper!
Before powering up your breadboard, ensure your power supply module's jumper cap is set to 5V.
The default is often 3.3V, but our components today require 5V for optimal performance and to avoid unexpected issues. Check for the small jumper cap on your power supply module and move it to the 5V position if it isn't already there.

## Slide 12
Phase 0 - Let's Build
Steps:
Connect power supply module to breadboard rails
Connect Arduino 5V to breadboard top rail
Connect Arduino GND to breadboard ground rail
Open Phase 0 code from GitHub
Upload and open Serial Monitor (9600 baud)
Verify "System Status: READY" messages
Success: You should see power verification messages every 2 seconds

## Slide 13
*wire colors in the diagrams are for visual reference only - general guidance = use the shortest wire that works

## Slide 14
Phase 0 - Let's Build
Steps:
1
Connect power supply module to breadboard rails
2
Connect Arduino 5V to breadboard top rail
3
Connect Arduino GND to breadboard ground rail
4
Copy Phase 0 code from GitHub
5
Upload and open Serial Monitor (9600 baud)
6
Verify "System Status: READY" messages
Success: You should see power verification messages every 2 seconds

## Slide 15
Phase 1 - First Light (Crawl)
Goal:
Make an LED blink
What You're Learning:
Basic circuit building
Digital pin control (Pin 13)
Non-blocking timing with millis()
Real-World Applications:
Smart home lighting
Notification systems
Status indicators

## Slide 16
Phase 1 - Components
What You Need:
1x Red LED
Jumper wires
Breadboard (already powered from Phase 0)
The Circuit:
Pin 13 → LED positive (long leg)
LED negative → Ground rail (direct connection, no resistor needed)

## Slide 17
Phase 1 - Let's Build
Steps:
1
Insert LED into breadboard
2
Connect Pin 13 to LED positive lead
3
Connect LED negative to ground rail
4
Open Phase 1 code from GitHub
5
Upload to Arduino
6
Watch it blink! (500ms on, 500ms off)
Serial Monitor: Shows LED state changes with timestamps

## Slide 18
What You Need:
1x Red LED
Jumper wires
Breadboard (already powered from Phase 0)
The Circuit:
Pin 13 → LED positive (long leg)
LED negative → Ground rail (direct connection, no resistor needed)

## Slide 19
Phase 1 - Let's Build
Steps:
1
Insert LED into breadboard
2
Connect Pin 13 to LED positive lead
3
Connect LED negative to ground rail
4
Open Phase 1 code from GitHub
5
Upload to Arduino
6
Watch it blink! (500ms on,
500ms off)
Serial Monitor: Shows LED state changes with timestamps

## Slide 20
Phase 2 - Button Control (Walk)
Goal:
Button toggles LED on/off with buzzer feedback
What You're Learning:
Reading digital inputs (buttons)
INPUT_PULLUP resistor configuration
Controlling multiple outputs
State management
Real-World Applications:
Light switches
Alarm systems with user control
Interactive devices

## Slide 21
Phase 2 - Components
What You Need:
Red LED (from Phase 1 - keep it connected!)
1x Push Button
1x Active Buzzer
Jumper wires
New Connections:
Pin 7 → Buzzer positive
Buzzer negative → Ground
Pin 8 → Button terminal
Button other terminal → Ground

## Slide 22
Phase 2 - Let's Build
Steps:
1
Keep Phase 1 LED connected
2
Add button between Pin 8 and ground
3
Add buzzer between Pin 7 and ground
4
Copy Phase 2 code from GitHub
5
Upload and test!
Expected Behavior:
Press button → LED toggles + buzzer beeps
Press again → LED toggles opposite way + beep

## Slide 23
What You Need:
Green LED (from Phase 1 - keep it connected!)
1x Push Button
1x Active Buzzer
Jumper wires
New Connections:
Pin 7 → Buzzer positive
Buzzer negative → Ground
Pin 8 → Button terminal
Button other terminal → Ground

## Slide 24
Phase 2 - Let's Build
Steps:
1
Keep Phase 1 LED connected
2
Add button between Pin 8 and ground
3
Add buzzer between Pin 7 and ground
4
Open Phase 2 code from GitHub
5
Upload and test!
Expected Behavior:
Press button → LED toggles + buzzer beeps
Press again → LED toggles opposite way + beep

## Slide 25
Phase 3 - Proximity Alarm (CHAOS)
Goal:
Distance-sensing alarm system that beeps faster as objects approach
What You're Learning:
Ultrasonic distance measurement
Shift register control for displays
Display multiplexing
Variable alarm behavior based on sensor input
Complete system integration
Real-World Applications:
Car parking sensors (backup alarms)
Security/intrusion detection
Automated door systems

## Slide 26
Phase 3 - The Complete System
This is a FULL IoT system with:
Input:
Ultrasonic sensor measures distance (2-400cm)
Processing:
Arduino calculates beep rate based on distance
Outputs:
4-digit display shows distance in cm
LED lights at ≤5cm
Buzzer beeps at ≤10cm (faster as distance decreases)
Mute button for buzzer control

## Slide 27
Phase 3 - Components
What You Need:
HC-SR04 Ultrasonic Sensor
4-Digit 7-Segment Display
74HC595 Shift Register (may be built into display)
LED, Buzzer, Button (from Phase 2 - keep connected!)
Multiple jumper wires
Complex Wiring: This is the most involved - take your time!

## Slide 28
Phase 3 - Critical Connections
Shift Register & Display:
Pin 4 → Data
Pin 5 → Latch
Pin 6 → Clock
Pins 9-12 → Display common cathodes
Ultrasonic Sensor:
Pin 2 → TRIG
Pin 3 → ECHO
VCC → 5V rail
GND → Ground rail
Keep Phase 2 components: Pin 7 (buzzer), Pin 8 (button), Pin 13 (LED)

## Slide 29
Phase 3 - Let's Build
Steps:
1
Add 4-digit display with shift register connections
2
Add ultrasonic sensor (TRIG to Pin 2, ECHO to Pin 3)
3
Verify all Phase 2 components still connected
4
Copy Phase 3 code from GitHub
5
Upload and test!
Testing:
Move your hand toward/away from sensor
Display shows distance in cm
LED lights at ≤5cm
Buzzer beeps at ≤10cm (faster = closer)
Button mutes/unmutes buzzer

## Slide 31
Phase 3 - Let's Build
Steps:
1
Add 4-digit display with shift register connections
2
Add ultrasonic sensor (TRIG to Pin 2, ECHO to Pin 3)
3
Verify all Phase 2 components still connected
4
Copy Phase 3 code from GitHub
5
Upload and test!
Testing:
Move your hand toward/away from sensor
Display shows distance in cm
LED lights at ≤5cm
Buzzer beeps at ≤10cm (faster = closer)
Button mutes/unmutes buzzer

## Slide 32
Quick Check
Phase 3 Status Check:
👍 Working?
Experiment with different distances!
🤔 Still building?
Keep going - this is the complex one!
❌ Having issues?
Common problems in troubleshooting guide
Everyone's at different stages - that's completely normal!

## Slide 33
What You Built Today
Four Progressive Systems:
Power verification - Foundation for everything
Simple output control - LED blinking (processor → output)
Interactive control - Button input with multiple outputs (input → processor → outputs)
Autonomous sensor system - Distance-based alarm with display (sensor → processor → multiple outputs)
The Evolution: From simple blink to complete IoT automation!

## Slide 34
The Building Block Approach
Phase 1:
OUTPUT only (LED)
Phase 2:
INPUT + OUTPUTS (button → LED + buzzer)
Phase 3:
SENSOR + PROCESSING + MULTIPLE OUTPUTS (ultrasonic → Arduino logic → display + LED + buzzer)
This is how ALL IoT systems work
- just different combinations of these same building blocks!

## Slide 35
The Flexibility of Arduino
Same Arduino, Endless Possibilities:
Home automation systems
Weather stations
Robots and drones
Art installations
Wearable tech
Industrial monitoring
Your kit has even more: Temperature sensors, servo motors, LCD display, IR receiver, relay...

## Slide 36
Resources & Next Steps
GitHub Repository:
https://tinyurl.com/5fan5erw
All Phase 0-3 code
Wiring diagrams for each phase
Component specifications
Detailed troubleshooting guide
Keep Learning:
Arduino official tutorials (arduino.cc)
Online communities (Arduino forums, Reddit r/arduino)
Experiment with other components in your kit!

## Slide 37
Q&A / Troubleshooting
Questions?
About what we built today
Component functionality
Where to go next
Troubleshooting your Phase 3 build
Still working on Phase 3? Keep building - we're here to help!

## Slide 38
Wire We Doing This?
Thanks for building IoT systems with us today!
Resources: https://tinyurl.com/5fan5erw
Questions: jowen@ftsc.com apatel@ftsc.com
Happy tinkering! 🔧⚡