## Slide 1
Wire We Doing This?
Building IoT Systems from Scratch
F-Con 2025

## Slide 2
Today's Journey
What We're Building:
Phase 0: Power test & connectivity (Setup)
Phase 1: Blink an LED (Crawl)
Phase 2: Button control with feedback (Walk)
Phase 3: Distance-sensing proximity alarm (Run)
The Goal: Understand how sensors, processors, and outputs work together to create IoT systems

## Slide 3
What's In Your Kit?
Key Components We're Using Today:
Arduino Uno - Your programmable brain
Breadboard & Prototype Shield - Your workspace
Power Supply Module - Clean 5V power distribution
Green LED - Visual output
Active Buzzer - Audio alerts
Push Button - User input
HC-SR04 Ultrasonic Sensor - Distance measurement
4-Digit 7-Segment Display - Numerical readout
74HC595 Shift Register - Efficient display control
Supporting cast: 220Ω resistors, jumper wires

## Slide 4
Arduino 101
What is Arduino?
A microcontroller board that:
Reads inputs (buttons, sensors, signals)
Processes information (runs your code)
Controls outputs (lights, displays, buzzers)
Why Arduino?
Easy to learn
Massive community support
Powers everything from hobby projects to commercial products

## Slide 5
The IoT Building Block Concept
SENSOR
Gather information (distance, temperature, motion)
PROCESSOR
Make decisions (Arduino analyzes the data)
OUTPUT
Take action (displays, buzzers, lights)
Every IoT device follows this pattern. Today you'll build increasingly complex systems using this exact pattern.

## Slide 6
Setup Check
Before We Start:
Kit contents verified
Arduino IDE installed and open
Arduino connected via USB
GitHub repository link ready
GitHub Resources: https://tinyurl.com/5fan5erw All code, wiring diagrams, and troubleshooting guides
https://github.com/Fulcrum-Technology-Solutions/fcon_2025_iotoys

## Slide 7
Phase 0 - Power Test (Setup)
Goal:
Verify everything is connected and powered correctly
What You're Learning:
Breadboard power distribution
Arduino connectivity
Serial communication basics
Why This Matters:
A solid power foundation prevents 90% of problems!

## Slide 8
Phase 0 - Let's Build
Steps:
01
Connect power supply module to breadboard rails
02
Connect Arduino 5V to breadboard top rail
03
Connect Arduino GND to breadboard ground rail
04
Copy Phase 0 code from GitHub
05
Upload and open Serial Monitor (9600 baud)
06
Verify "System Status: READY" messages
Success: You should see power verification messages every 2 seconds

## Slide 10
Phase 1 - First Light (Crawl)
Goal:
Make an LED blink
What You're Learning:
Basic circuit building
Digital pin control (Pin 13)
Non-blocking timing with millis()
Real-World Applications:
Smart home lighting
Notification systems
Status indicators

## Slide 11
Phase 1 - Components
What You Need:
1x Red LED
Jumper wires
Breadboard (already powered from Phase 0)
The Circuit:
Pin 13 → LED positive (long leg)
LED negative → Ground rail (direct connection, no resistor needed)

## Slide 12
Phase 1 - Let's Build
Steps:
01
Insert LED into breadboard
02
Connect Pin 13 to LED positive lead
03
Connect LED negative to ground rail
04
Copy Phase 1 code from GitHub
05
Upload to Arduino
06
Watch it blink! (500ms on, 500ms off)
Serial Monitor: Shows LED state changes with timestamps

## Slide 13
What You Need:
1x Red LED
Jumper wires
Breadboard (already powered from Phase 0)
The Circuit:
Pin 13 → LED positive (long leg)
LED negative → Ground rail (direct connection, no resistor needed)

## Slide 14
Phase 2 - Button Control (Walk)
Goal:
Button toggles LED on/off with buzzer feedback
What You're Learning:
Reading digital inputs (buttons)
INPUT_PULLUP resistor configuration
Controlling multiple outputs
State management
Real-World Applications:
Light switches
Alarm systems with user control
Interactive devices

## Slide 15
Phase 2 - Components
What You Need:
Red LED (from Phase 1 - keep it connected!)
1x Push Button
1x Active Buzzer
Jumper wires
New Connections:
Pin 7 → Buzzer positive
Buzzer negative → Ground
Pin 8 → Button terminal
Button other terminal → Ground

## Slide 16
Phase 2 - Let's Build
Steps:
01
Keep Phase 1 LED connected
02
Add button between Pin 8 and ground
03
Add buzzer between Pin 7 and ground
04
Copy Phase 2 code from GitHub
05
Upload and test!
Expected Behavior:
Press button → LED toggles + buzzer beeps
Press again → LED toggles opposite way + beep

## Slide 17
What You Need:
Green LED (from Phase 1 - keep it connected!)
1x Push Button
1x Active Buzzer
Jumper wires
New Connections:
Pin 7 → Buzzer positive
Buzzer negative → Ground
Pin 8 → Button terminal
Button other terminal → Ground

## Slide 18
Phase 3 - Proximity Alarm (Run)
Goal:
Distance-sensing alarm system that beeps faster as objects approach
What You're Learning:
Ultrasonic distance measurement
Shift register control for displays
Display multiplexing
Variable alarm behavior based on sensor input
Complete system integration
Real-World Applications:
Car parking sensors (backup alarms)
Security/intrusion detection
Automated door systems

## Slide 19
Phase 3 - The Complete System
This is a FULL IoT system with:
Input:
Ultrasonic sensor measures distance (2-400cm)
Processing:
Arduino calculates beep rate based on distance
Outputs:
4-digit display shows distance in cm
LED lights at ≤5cm
Buzzer beeps at ≤10cm (faster as distance decreases)
Mute button for buzzer control

## Slide 20
Phase 3 - Components
What You Need:
HC-SR04 Ultrasonic Sensor
4-Digit 7-Segment Display
74HC595 Shift Register (may be built into display)
LED, Buzzer, Button (from Phase 2 - keep connected!)
Multiple jumper wires
Complex Wiring: This is the most involved - take your time!

## Slide 21
Phase 3 - Critical Connections
Shift Register & Display:
Pin 4 → Data
Pin 5 → Latch
Pin 6 → Clock
Pins 9-12 → Display common cathodes
Ultrasonic Sensor:
Pin 2 → TRIG
Pin 3 → ECHO
VCC → 5V rail
GND → Ground rail
Keep Phase 2 components: Pin 7 (buzzer), Pin 8 (button), Pin 13 (LED)

## Slide 22
Phase 3 - Let's Build
Steps:
01
Add 4-digit display with shift register connections
02
Add ultrasonic sensor (TRIG to Pin 2, ECHO to Pin 3)
03
Verify all Phase 2 components still connected
04
Copy Phase 3 code from GitHub
05
Upload and test!
Testing:
Move your hand toward/away from sensor
Display shows distance in cm
LED lights at ≤5cm
Buzzer beeps at ≤10cm (faster = closer)
Button mutes/unmutes buzzer

## Slide 24
Quick Check
Phase 3 Status Check:
👍 Working?
Experiment with different distances!
🤔 Still building?
Keep going - this is the complex one!
❌ Having issues?
Common problems in troubleshooting guide
Everyone's at different stages - that's completely normal!

## Slide 25
What You Built Today
Four Progressive Systems:
Power verification - Foundation for everything
Simple output control - LED blinking (processor → output)
Interactive control - Button input with multiple outputs (input → processor → outputs)
Autonomous sensor system - Distance-based alarm with display (sensor → processor → multiple outputs)
The Evolution: From simple blink to complete IoT automation!

## Slide 26
The Building Block Approach
Phase 1:
OUTPUT only (LED)
Phase 2:
INPUT + OUTPUTS (button → LED + buzzer)
Phase 3:
SENSOR + PROCESSING + MULTIPLE OUTPUTS (ultrasonic → Arduino logic → display + LED + buzzer)
This is how ALL IoT systems work
- just different combinations of these same building blocks!

## Slide 27
The Flexibility of Arduino
Same Arduino, Endless Possibilities:
Home automation systems
Weather stations
Robots and drones
Art installations
Wearable tech
Industrial monitoring
Your kit has even more: Temperature sensors, servo motors, LCD display, IR receiver, relay...

## Slide 28
Resources & Next Steps
GitHub Repository:
https://tinyurl.com/5fan5erw
All Phase 0-3 code
Wiring diagrams for each phase
Component specifications
Detailed troubleshooting guide
Keep Learning:
Arduino official tutorials (arduino.cc)
Online communities (Arduino forums, Reddit r/arduino)
Experiment with other components in your kit!

## Slide 29
Q&A / Troubleshooting
Questions?
About what we built today
Component functionality
Where to go next
Troubleshooting your Phase 3 build
Still working on Phase 3? Keep building - we're here to help!

## Slide 30
Wire We Doing This?
Thanks for building IoT systems with us today!
Resources: https://tinyurl.com/5fan5erw
Questions: jowen@ftsc.com apatel@ftsc.com
Happy tinkering! 🔧⚡